Gilbert River Dam – 300 000 ML Storage

Estimate

PG 2/11/2010

Based on SunWater Estimate – Aug 2010

| Description | Unit | Quantity | Rate $ | Amount |
| --- | --- | --- | --- | --- |
| Direct Costs |  |  |  |  |
| Initial works |  |  |  |  |
| Erosion and Sediment Control Works | Item | 1 | 250 000 | 250 000 |
| Environmental protection and monitoring | Item | 1 | 200 000 | 200 000 |
| Clear Site and Inundated Area | ha | 1500 | 500 | 750 000 |
| Site Access Road | km | 25 | 200 000 | 5 000 000 |
| Road Relocation | km | 20 | 200 000 | 4 000 000 |
| Concrete Aggregate Preparations | Item | 1 | 1 050 000 | 1 050 000 |
| Haul Roads | km | 10 | 400 000 | 4 000 000 |
| Concrete Plant Operations | Item | 1 | 1 600 000 | 1 600 000 |
| River Care and Diversion | Item | 1 | 2 900 000 | 2 900 000 |
| Foundation Excavation and Preparation | Item | 1 | 6 800 000 | 6 800 000 |
| Foundation Grouting | Item | 1 | 1 100 000 | 1 100 000 |
| RCC Dam | m 3 | 225 000 | 200 | 45 000 000 |
| Spillway | m 3 | 7 230 | 760 | 5 500 000 |
| Outlet works -Concrete | m 3 | 9 600 | 1 136 | 10 900 000 |
| Outlet works - Metalwork | tonne | 151 | 13 245 | 2 000 000 |
| Outlet Works – M&E | Item | 2 | 970 000 | 1 940 000 |
| Site Services | Item | 1 | 1 500 000 | 1 500 000 |
| Sub Total |  |  |  | 94 490 000 |
| Indirect Costs |  |  |  |  |
| Site Overheads | 10% Direct Costs |  |  | 9 449 000 |
| WHS | Item |  |  | 600 000 |
| Environmental Compliance | Item |  |  | 250 000 |
| Insurance | Insurances |  |  | 1 200 000 |
| Wet Weather | Item |  |  | 800 000 |
| Camp Costs | 5% Direct Costs |  |  | 4 724 000 |
| Diesel Generator |  |  |  | 1 000 000 |
| Profit and offsite oveheads | 10% Direct Costs |  |  | 9 449 000 |
| Sub Total |  |  |  | 27 472 000 |
| Owner Costs |  |  |  |  |
| Concept/Preliminary Design | Item | 1 | 2 000 000 | 2 000 000 |
| Hydrology | Item | 1 | 350 000 | 350 000 |
| Geotech | Item | 1 | 1 500 000 | 1 500 000 |
| Final Design | 3% Direct Costs | Amount |  |  |
| RCC Mix Design | Item | 1 | 500 000 | 500 000 |
| EIS | Item | 1 | 7 000 000 | 7 000 000 |
| CHMP | Item | 1 | 3 300 000 | 3 300 000 |
| Land Acquisition | Item | 1 | 5 250 000 | 5 250 000 |
| Consultation | Item | 1 | 400 000 | 400 000 |
| Commissioning | 0.5% Direct Costs |  |  | 472 000 |
| Sub Total |  |  |  | 20 772 000 |
| Contingency |  | 20% Direct Costs |  | 18 898 000 |
| Total Project Cost |  |  |  | 161 632 000 |